## Slide 1: SHRIMP FARM PROJECT IN MANNAR

## Slide 2: SHRIMP FARM DESIGN – A MODEL

## Slide 4: PRAWN FARMING SYSTEMS
OPEN SYSTEM
SEMI CLOSED SYSTEM
CLOSED SYSTEM

## Slide 5: OPEN SYSTEM
Water taken from Water Source Directly to the Culture Ponds
Aeration or without aeration
No Disinfection Facilities before stocking
No Probiotic
No Bio Security Measures
No Technician or Technical Advisors

## Slide 6: SUSTAINABLE SHRIMP FARMING IN THE NOTHERN PROVINCE
OPEN SYSTEM
in
PRAWN FARMING
NOT RECCOMENDED

## Slide 7: SEMI CLOSED SYSTEM
Water Taken from the Water Source to the Storage Tank
Disinfection is done before using to the Grow Out Ponds
Limited release of water to the Natural Water Body.
Less Water Usage
Aeration
Probiotic Usage
Bio Security measures
Sedimentation Pond
Laboratory equipments available
Technical Advisor or Technician

## Slide 8: CLOSED SYSTEM
Water Taken from the Water Source to the Storage Tank at the inception only.
Disinfection is done before using to the Grow Out Ponds
No release of water to the Natural Water Body during the culture period.
Aeration
Probiotic Usage
Bio Security measures such as Bird Netting, Crab Fencing etc
Drainage Water is sent through Sedimentation Pond and reused again.
Technical Advisor or Technician
Laboratory Facilities

## Slide 9: SUSTAINABLE SHRIMP FARMING IN THE NORTHERN PROVINCE
SEMI CLOSED & CLOSED SYSTEMS
IN
PRAWN FARMING
RECCOMENDED

## Slide 10: POND PREPARATION
Dry Period Should be at least 2 Months
Sludge Should Be Removed from the Pond Bottom after Drying
Pond Dykes should be repaired to maintain minimum of 1 m water depth.
Inlet and Out Let Structures to be repaired
Bottom to be Ploughed
According to the pH, lime or dolomite to be applied
Necessary Equipments to be organized e.g.: Tray Bridge, Paddle Wheel Aerators, Feed Trays etc
Bio Security Measures to be implemented e.g.: Bird Netting, Crab Fencing etc

## Slide 11: BIO SECURITY MEASURES
Fencing around the Farm
Gate at the entrance of the Farm
Foot Bath at the Farm Gate for disinfection of Vehicles
Foot Bath for workers before entering ponds
Removal of Crabs and Crab Fencing
Bird Netting
Obtaining the Approval from NAQDA officer with the concurrence of the relevant Farming Society is a must before water filling.

## Slide 12: WATER FILLING
Use Filter Bag to Pump the water from the Natural Water Body
Fill the Water in to the Reservoir Tank
Disinfect the water in the Reservoir Tank
Pump the Water to the Grow out pond from the reservoir Tank
Use necessary fertilizer to maintain the algal bloom in the Pond before stocking
Monitor Water Quality for Ammonia, pH, Salinity etc

## Slide 13: POST LARVAE SELECTION
Selection of Good Quality Post Larvae is very important for Successful Prawn Farming
Select a Prawn Hatchery with good management practices to buy Post larvae
Check the sample of post larvae from the Hatchery Tank in a reputed laboratory
Post Larvae should be checked for Quality Standards and PCR tests should be carried out to detect any virus infections such as WSSV and MBV etc.
The above laboratory report should be submitted to obtain the Post Larvae Stocking Bills from NAQDA.
The Post Larvae Stocking Bills issued by NAQDA should be produced to the hatchery to release the PLs to the particular Prawn Farm
The salinity and pH reading should be informed to the Hatchery for acclimatization of the PLs in the Hatchery.
Good quality and disease free PL 15 to PL 20 can be stocked in the Ponds

## Slide 14: POST LARVAE TRANSPORT
PL transportation should be done during the low temperature period of the day – Before 8 am or after 4 pm
Direct sunlight should not fall in to the Post Larvae during transport.
Pls should not be transported in Air tight lorries as at may increase the temperature inside the cabin of the Lorry
During the high temperature periods, ice should be used in a proper way to maintain suitable temperature in the PL Bags.

## Slide 15: POST LARVAE STOCKING
The Stocking of the Open System without aeration should be around 4 – 6 Pls per Sq M
Open System Farms with Aeration can be stocked 15 per Sq. M - Not Suitable for Sustainable Shrimp Farming
Semi Closed and Closed System farms can be stocked with 15 to 25 Pls per Sq M
Nursery ponds can be stocked with higher densities, but the Juveniles should be transferred between 30 to 45 days to the Grow out ponds
Post Larvae can be stocked in the morning or evening
If any difference in water quality parameters in the pond and inside PLs bag, the acclimatization should be done prior stocking

## Slide 16: FEED MANAGEMENT
The Farmers should use the Prawn Feed Approved by the Department of Animal Production and Health of Sri Lanka
Feeding of the Prawns depends on various factors such as temperature, rain fall, molt etc.
Feeding tray should be carefully monitored to evaluate the feed requirement of the pond for the particular day – Do not depend the feeding guide only
Feed should be stored in the farm in proper manner.
Prawn Feed cost is around 55 – 65 % of the total production cost. – So The Feed Management is very important in Shrimp Farming

## Slide 17: POND WATER AND PRAWN HEALTH MANAGEMENT
Maintaining good water quality in the ponds will induce the good growth and minimize the risk for the diseases
Higher percentage of water exchanges will harm the environment and increase the cost of production.
The better way is to use Probiotics to maintain the water quality.
Probiotics will prevent the growth of harmful bacteria in the ponds and improves the pond bottom conditions.
Monitoring the weight and health of the Prawns weekly for any abnormalities and seek technical advice
Record Keeping

## Slide 18: WATER MANAGEMENT
The water quality parameters should be monitored regularly
Vibrio Bacterial Monitoring should be done once in two weeks
Maintain all the quality monitoring information
Take remedial action according to the technical advice

## Slide 19: WATER QUALITY MONITORING
PARAMETERS | MONITORING TIME | SUITABLE RANGE
pH | Morning 7.00 am to 8.00 am Evening 4.00 pm to 5.00 pm | 7.5 – 8.5
Salinity | Weekly | 10 – 30 ppt
Alkalinity | Weekly | Above 80 ppm
Secchi Disc Reading | 11.00 am | 30 – 40 cm
Ammonia | Weekly | Below 0.1 ppm
Dissolved Oxygen | Any time of the Day | Above 4.0 ppm

## Slide 20: DISEASES REPORTING
If any occurrence of disease like WSSV please report to the relevant Farm Society and NAQDA Officer
Raise a RED FLAG to alert the other farmers
Stop Water Exchanges
Prevent the release of water to the natural water body
Inform the adjoining farms in the area.

## Slide 21: SEDIMENTATION TANK
Sedimentation tank is a must in a prawn farm
Small Farms can use common sedimentation tank constructed in their area
Sedimentation Tank capacity should be 10% of the total Pond Volume
Depth should be 1.0 m deeper than the grow out ponds
Clams or other filter feeders can be grown to purify the drainage water
Fishing should not be allowed in the sedimentation Tank during the culture period

## Slide 22: HARVEST AND POST HARVEST HANDLING
Pond Harvest should be planned after considering the Market Factors
High quality of the shrimps will fetch the higher prices
Big Size shrimps also fetch higher Prices
Shrimps should be killed in the ice water to maintain the high quality
If the head of the shrimp is not good, it has to be removed before exports – We loose the money for the head – around 35 to 38%
If the shell or tail is damaged, shell and tail will have to be removed in addition to head. – We loose 50 %

## Slide 23: Factors Affecting the Profitability of the Prawn Farming in Sri Lanka
Market Price of the Prawns
Cost of Inputs such as Prawn Fry, Prawn Feed, Cost of Electricity/Fuel and Salaries etc
Risk factors – Flood, Cyclone etc
Production Loss due to diseases
Law and Order of the Country

## Slide 24: SHRIMP FARMING IN MANNAR
Country: Sri Lanka
Province: Northern Province
District: Mannar
DS Division: Nanattan
GN Division: Pasikkulam
Total Land Area Proposed 200 Acres (80Ha)
Land For Model Farm 50 Acres (20 Ha)
Land for Community Support Farm 150 Acres(60 Ha)

## Slide 25: PROPOSED PROJECT IMPLEMENTATION
Model Farm will be established and operated by the Investor
Community Support Farm will be established by the Investor and selected beneficiaries from the Area by forming a separate entity.
80% Shares for the Investor and the balance 20% for the beneficiaries.

## Slide 26: INVESTMENT PLANS
100% investment for the Model Farm by the Investor.
80% of the capital Investment of the Community Support Farm by the Investor and the balance 20% will have to be invested by the beneficiaries from the funds they receive in the form of a grant or soft loan from the bank.(Rs 300,000 per beneficiary)
Total number of beneficiaries 92
The total working capital will have to be provided by the investor.

## Slide 27: ECONOMICS OF 50 ACRE MODEL SHRIMP FARM

## Slide 28: FARM DESIGN & CONSTRUCTION ASSUMPTIONS 50 ACRE MODEL FARM
Crops per Year | 2 | Nos
Total No of Grow out Ponds | 20 | Nos
Average Pond Area | 0.5 | Hactare
Stocking Density | 20 | Pl/SqM
Survival Rate | 80 | %
Feed Conversion Ratio (FCR) | 1.5 | 
Lime/Dolomite | 3000 | Kg/Pond
Fertilizers | 50 | Kg/Pond
Water Exchanges | 5 | %/Day
Average Weight at Harvest | 35 | g
Culture Period | 120 | Days
Pond Preparation/Drying Period | 60 | Days
General Manager | 1 | Nos
Biologist | 1 | Nos
Electrician | 1 | Nos
Supervisors | 3 | Nos
Pond Workers | 15 | Nos

## Slide 29: FINANCIAL ASSUMPTIONS (RS) 50 ACRE MODEL FARM
Market Price of 35 g Prawns per Kg | 850.00
Post Larvae | 0.75
Prawn Feed per Kg | 200.00
Lime/Dolomite per Kg | 5.00
Fertilizers per kg | 100.00
Pond Preparation per one Grow Out pond | 40,000.00
Probiotic Culture per Grow out Pond | 40,000.00
Chemical and Medicines per Grow out Pond | 25,000.00
Electricity/Fuel per Grow out Pond | 100,000.00
Repairs and Maintenance per Grow out Pond | 30,000.00
Transport Expenses per Grow out Pond | 20,000.00
Grow Out Harvest expenses | 25,000.00
General Manager's Salary/month | 65,000.00
Biologist's Salary/month | 40,000.00
Electrician's Salary/month | 30,000.00
Supervisors Salary/month | 25,000.00
Pond Workers Salary/month | 18,000.00
Staff Welfare per Pond/month | 6,000.00
Lease Rental for the Land per annum | 300,000.00
Legal/Licensing Expenses per annum | 100,000.00
Office & Misc Expenses Per Pond per month | 5,000.00
Farmers Training Program per month | 5,000.00
NAQDA Staff Traning Program | 5,000.00
Research & Development per month | 25,000.00
Accounts & audut Fees per month | 15,000.00
Insurance per annum | 200,000.00

## Slide 30: CAPITAL INVESTMENTS (RS) 50 ACRE MODEL FARM
Details/Items Required | No of Unites | Unit Cost (Rs) | Total Expenditure (Rs)
Reservoir Pond Construction (Earth Work) | 1 | 1,000,000.00 | 1,000,000.00
Grow out Pond Construction (Earth Work) | 20 | 600,000.00 | 12,000,000.00
Outlet Structures | 20 | 250,000.00 | 5,000,000.00
Inlet Structures | 20 | 50,000.00 | 1,000,000.00
Out let Canals | 1 | 1,200,000.00 | 1,200,000.00
Inlet Canals | 1 | 1,800,000.00 | 1,800,000.00
Environmental Mitigation | 1 | 300,000.00 | 300,000.00
Electrical Supply | 1 | 3,000,000.00 | 3,000,000.00
Internal Road Construction | 1 | 800,000.00 | 800,000.00
Generator 200 KVA | 1 | 1,800,000.00 | 1,800,000.00
Water Pumps (10" Submersible) | 5 | 180,000.00 | 900,000.00
PVC Items for the Water Pumps | 5 | 120,000.00 | 600,000.00
Switch Gears for Water Pumps | 5 | 25,000.00 | 125,000.00
Paddle Wheel Aerators 1 Hp | 80 | 65,000.00 | 5,200,000.00
Switch Gears for Paddle Wheel Aerators | 80 | 20,000.00 | 1,600,000.00
DO Meter (YSI Brand) | 1 | 55,000.00 | 55,000.00
Refracto Meter | 1 | 35,000.00 | 35,000.00
Water pH Meters | 1 | 12,000.00 | 12,000.00
Thermometer | 1 | 1,500.00 | 1,500.00
Water Quality Kits | 1 | 100,000.00 | 100,000.00
General Tool kit | 1 | 50,000.00 | 50,000.00
Office, Stores & Workers Temporary Huts | 1 | 300,000.00 | 300,000.00
Furniture and Fittings | 1 | 100,000.00 | 100,000.00
Kitchen Equipment | 1 | 50,000.00 | 50,000.00

## Slide 31: CAPITAL INVESTMENTS (RS) 50 ACRE MODEL FARM
5 Mt Fiberglass Tanks | 2 | 100,000.00 | 200,000.00
Air Blower 1 Hp | 2 | 40,000.00 | 80,000.00
Tray Bridges | 40 | 10,000.00 | 400,000.00
Feeding Trays | 40 | 2,000.00 | 80,000.00
Inlet Screens | 20 | 5,000.00 | 100,000.00
Outlet Screens | 20 | 18,000.00 | 360,000.00
Farm Internal wiring and Electrical Items | 20 | 45,000.00 | 900,000.00
Weighing Balance 25 Kg | 2 | 4,000.00 | 8,000.00
Sampling Balance 5 kg | 2 | 4,000.00 | 8,000.00
Feeding Buckets | 20 | 500.00 | 10,000.00
Feeding Scoops | 20 | 100.00 | 2,000.00
Cast Net | 2 | 3,000.00 | 6,000.00
Sampling Buckets | 2 | 1,000.00 | 2,000.00
Rechargeable Torches | 8 | 1,800.00 | 14,400.00
Rain Coats | 15 | 900.00 | 13,500.00
Two Wheel Tractor | 1 | 200,000.00 | 200,000.00
Push Bicycles | 1 | 10,000.00 | 10,000.00
Motor Bike | 1 | 175,000.00 | 175,000.00
Crew Cab | 1 | 1,500,000.00 | 1,500,000.00
TOTAL CAPITAL EXPENDITURE |  |  | 41,097,400.00

## Slide 32: WORKING CAPITAL FOR ONE CROP (RS) 50 ACRE MODEL FARM
Pond Preparation | 800,000.00
Prawn Feeds | 16,800,000.00
Lime/Dolomite | 300,000.00
Fertilizers | 100,000.00
Chemicals/Medicines | 500,000.00
Probiotic Cultures | 800,000.00
Electricity/Fuel | 2,000,000.00
Repairs and Maintenance | 600,000.00
Transport Expenses | 400,000.00
Harvest Expenses | 500,000.00
General Manager's Salary | 390,000.00
Biologist's Salary | 240,000.00
Electrician's Salary | 180,000.00
Supervisors' Salaries | 450,000.00
Pond Workers' Salaries | 1,620,000.00
Staff Welfare | 720,000.00
Lease Rental for the Land per annum | 300,000.00
Legal/Licensing Expenses | 100,000.00
Farmers Training Program | 30,000.00
NAQDA Staff Training Program | 30,000.00
Research & Development | 150,000.00
Accounts & audit Fees | 90,000.00
Insurance per annum | 100,000.00
Office & Misc. Expenses | 600,000.00
TOTAL WORKING CAPITAL FOR ONE CROP | 27,800,000.00

## Slide 33: INCOME & EXPENSES STATEMENT (RS) 50 ACRE MODEL FARM
Income | 
Prawn Sales | 95,200,000.00
Expenses | 
Pond Preparation | 1,600,000.00
Prawn Feeds | 33,600,000.00
Lime/Dolomite | 600,000.00
Fertilizers | 200,000.00
Chemicals/Medicines | 1,000,000.00
Probiotic Cultures | 1,600,000.00
Electricity/Fuel | 4,000,000.00
Repairs and Maintenance | 1,200,000.00
Transport Expenses | 800,000.00
Harvest Expenses | 1,000,000.00

## Slide 34: INCOME & EXPENSES STATEMENT (RS) 50 ACRE MODEL FARM
General Manager's Salary | 780,000.00
Biologist's Salary | 480,000.00
Electrician's Salary | 360,000.00
Supervisors' Salaries | 900,000.00
Pond Workers' Salaries | 3,240,000.00
Staff Welfare | 1,440,000.00
Lease Rental for the Land | 300,000.00
Legal/Licensing Expenses | 200,000.00
Farmers Training Program | 60,000.00
NAQDA Staff Training Program | 60,000.00
Research & Development | 300,000.00
Accounts & audit Fees | 180,000.00
Insurance | 100,000.00
Misc. Expenses | 1,200,000.00
Total Expenses | 55,200,000.00
Total Profit from One Year | 40,000,000.00
(The Financial Cost and Depreciation have not been included in the above calculations) | 

## Slide 35: INVESTMENT DECISIONS 50 ACRE MODEL FARM
Total Investment Required For Model farm | 68,897,400.00
Return on Investment (ROI) for Investors | 58.06
Pay Back Period (Years) | 1.72

## Slide 36: ECONOMICS OF COMMUNITY SUPPORT SHRIMP FARM 150 Acres

## Slide 37: FARM DESIGN & CONSTRUCTION ASSUMPTIONS COMMUNITY SUPPORT SHRIMP FARM
Crops per Year | 2 | Nos
Total No of Grow out Ponds | 46 | Nos
Average Pond Area | 0.5 | Hactare
Stocking Density | 20 | Pl/SqM
Survival Rate | 80 | %
Feed Conversion Ratio (FCR) | 1.5 | 
Lime/Dolomite | 3000 | Kg/Pond
Fertilizers | 50 | Kg/Pond
Water Exchanges | 5 | %/Day
Average Weight at Hatvest | 35 | g
Culture Period | 120 | Days
Pond Preparation/Drying Period | 60 | Days
General Manager | 1 | Nos
Biologist | 2 | Nos
Electrician | 2 | Nos
Supervisors | 4 | Nos
Pond Workers | 50 | Nos

## Slide 38: FINANCIAL ASSUMPTIONS (RS) COMMUNITY SUPPORT SHRIMP FARM
Market Price of 35 g Prawns per Kg |  | 850.00
Post Larvae |  | 0.75
Prawn Feed per Kg |  | 200.00
Lime/Dolomite per Kg |  | 5.00
Fertilizers per kg |  | 100.00
Pond Preparation per one Grow Out pond |  | 40,000.00
Probiotic Culture per Grow out Pond |  | 40,000.00
Chemical and Medicines per Grow out Pond |  | 25,000.00
Electricity/Fuel per Grow out Pond |  | 100,000.00
Repairs and Maintenance per Grow out Pond |  | 30,000.00
Transport Expenses per Grow out Pond |  | 20,000.00
Grow Out Harvest expenses |  | 25,000.00
General Manager's Salary/month |  | 65,000.00
Biologist's Salary/month |  | 40,000.00
Electrician's Salary/month |  | 30,000.00
Supervisors Salary/month |  | 25,000.00
Pond Workers Salary/month |  | 18,000.00
Staff Welfare per Pond/month |  | 6,000.00
Lease Rental for the Land per annum |  | 700,000.00
Legal/Licensing Expenses per annum |  | 250,000.00
Office & Misc. Expenses Per Pond per month |  | 5,000.00
Research & Development per month |  | 25,000.00
Accounts & audit Fees per month |  | 30,000.00
Insurance per annum |  | 500,000.00

## Slide 39: CAPITAL INVESTMENTS (RS) COMMUNITY SUPPORT SHRIMP FARM
Details/Items Required | No of Unites | Unit Cost (Rs) | Total Expenditure (Rs)
Reservoir Pond Construction (Earth Work) | 1 | 2,000,000.00 | 2,000,000.00
Grow out Pond Construction (Earth Work) | 46 | 600,000.00 | 27,600,000.00
Outlet Structures | 46 | 250,000.00 | 11,500,000.00
Inlet Structures | 46 | 50,000.00 | 2,300,000.00
Out let Canals | 1 | 2,200,000.00 | 2,200,000.00
Inlet Canals | 1 | 1,200,000.00 | 1,200,000.00
Environmental Mitigation | 1 | 1,000,000.00 | 1,000,000.00
Electrical Supply | 1 | 5,000,000.00 | 5,000,000.00
Internal Road Construction | 1 | 1,200,000.00 | 1,200,000.00
Generator 200 KVA | 2 | 1,800,000.00 | 3,600,000.00
Water Pumps (6" Submersible) | 46 | 90,000.00 | 4,140,000.00
PVC Items for the Water Pumps | 46 | 40,000.00 | 1,840,000.00
Switch Gears for Water Pumps | 46 | 25,000.00 | 1,150,000.00
Paddle Wheel Aerators 1 Hp | 184 | 65,000.00 | 11,960,000.00
Switch Gears for Paddle Wheel Aerators | 184 | 20,000.00 | 3,680,000.00
DO Meter (YSI Brand) | 2 | 55,000.00 | 110,000.00
Refracto Meter | 2 | 35,000.00 | 70,000.00
Water pH Meters | 2 | 12,000.00 | 24,000.00
Thermometer | 2 | 1,500.00 | 3,000.00
Water Quality Kits | 2 | 100,000.00 | 200,000.00
General Tool kit | 2 | 50,000.00 | 100,000.00
Office, Stores & Workers Temporary Huts | 2 | 300,000.00 | 600,000.00
Furniture and Fittings | 2 | 100,000.00 | 200,000.00
Kitchen Equipment | 2 | 50,000.00 | 100,000.00

## Slide 40: CAPITAL INVESTMENTS (RS) COMMUNITY SUPPORT SHRIMP FARM
5 Mt Fiberglass Tanks | 4 | 100,000.00 | 400,000.00
Air Blower 1 Hp | 4 | 40,000.00 | 160,000.00
Tray Bridges | 92 | 10,000.00 | 920,000.00
Feeding Trays | 92 | 2,000.00 | 184,000.00
Inlet Screens | 46 | 5,000.00 | 230,000.00
Outlet Screens | 46 | 18,000.00 | 828,000.00
Farm Internal wiring and Electrical Items | 46 | 45,000.00 | 2,070,000.00
Weighing Balance 25 Kg | 4 | 4,000.00 | 16,000.00
Sampling Balance 5 kg | 4 | 4,000.00 | 16,000.00
Feeding Buckets | 46 | 500.00 | 23,000.00
Feeding Scoops | 46 | 100.00 | 4,600.00
Cast Net | 4 | 3,000.00 | 12,000.00
Sampling Buckets | 4 | 1,000.00 | 4,000.00
Rechargeable Torches | 16 | 1,800.00 | 28,800.00
Rain Coats | 30 | 900.00 | 27,000.00
Two Wheel Tractor | 2 | 200,000.00 | 400,000.00
Push Bicycles | 2 | 10,000.00 | 20,000.00
Motor Bike | 2 | 175,000.00 | 350,000.00
Crew Cab | 1 | 1,500,000.00 | 1,500,000.00
TOTAL CAPITAL EXPENDITURE |  |  | 88,970,400.00

## Slide 41: WORKING CAPITAL FOR ONE CROP (RS) COMMUNITY SUPPORT SHRIMP FARM
Pond Preparation | 1,840,000.00
Prawn Feeds | 38,640,000.00
Lime/Dolomite | 690,000.00
Fertilizers | 230,000.00
Chemicals/Medicines | 1,150,000.00
Probiotic Cultures | 1,840,000.00
Electricity/Fuel | 4,600,000.00
Repairs and Maintenance | 1,380,000.00
Transport Expenses | 920,000.00
Harvest Expenses | 1,150,000.00
General Manager's Salary | 390,000.00
Biologist's Salary | 480,000.00
Electrician's Salary | 360,000.00
Supervisors' Salaries | 600,000.00
Pond Workers' Salaries | 5,400,000.00
Staff Welfare | 1,656,000.00
Lease Rental for the Land per annum | 300,000.00
Legal/Licensing Expenses | 100,000.00
Research & Development | 150,000.00
Accounts & audit Fees | 180,000.00
Insurance per annum | 500,000.00
Office & Misc. Expenses | 1,380,000.00
TOTAL WORKING CAPITAL FOR ONE CROP | 63,936,000.00

## Slide 42: INCOME & EXPENSES STATEMENT (RS) COMMUNITY SUPPORT SHRIMP FARM
Income | 
Prawn Sales | 218,960,000.00
Expenses | 
Pond Preparation | 3,680,000.00
Prawn Feeds | 77,280,000.00
Lime/Dolomite | 1,380,000.00
Fertilizers | 460,000.00
Chemicals/Medicines | 2,300,000.00
Probiotic Cultures | 3,680,000.00
Electricity/Fuel | 9,200,000.00
Repairs and Maintenance | 2,760,000.00
Transport Expenses | 1,840,000.00
Harvest Expenses | 2,300,000.00

## Slide 43: INCOME & EXPENSES STATEMENT (RS) COMMUNITY SUPPORT FARM
General Manager's Salary | 780,000.00
Biologist's Salary | 960,000.00
Electrician's Salary | 720,000.00
Supervisors' Salaries | 1,200,000.00
Pond Workers' Salaries | 10,800,000.00
Staff Welfare | 3,312,000.00
Lease Rental for the Land | 300,000.00
Legal/Licensing Expenses | 200,000.00
Research & Development | 300,000.00
Accounts & audit Fees | 180,000.00
Insurance | 500,000.00
Misc. Expenses | 2,760,000.00
Total Expenses | 126,892,000.00
Total Profit from One Year | 92,068,000.00
(The Financial Cost and Depreciation have not been included in the above calculations) | 

## Slide 44: COMMUNITY SUPPORT SCHEME INVESTMENT DECISIONS COMMUNITY SUPPORT SHRIMP FARM
Community Support Scheme | 
% Profit Shared with local Community | 20%
% Profit to the Investor | 80%
No of Beneficiaries in the Project | 92
INVESTMENT DECISIONS | 
Total Investment Required | 152,906,400.00
Return on Investment (ROI) for investors | 48.17
Pay Back Period (Years) | 2.08